Feature （功能）

●  Resettable over current and over temperature protection            ●  Small size of 1206

过流、过温保护、可恢复                                                  封装尺寸1206

●  Fast time-to-trip                                                ●  Small footprint

快速保护                                                       占用空间小

●  RoHS complaint                                                ●  Low resistance

通过RoHS                                                      低电阻

Application （应用领域）

●  Computer                    ●   Industrial controls                  ●   Multimedia

计算机                           工业控制                             多媒体

●  Battery                        ●   Automotive                        ●   Game machines

电池                              汽车                                游戏机

●  Mobie phones                ●   Portable electronics                 ●   Telephony and broadband

移动电话                         便携式电子产品                       电话和宽带

Part Numbering （命名规则）

Product Dimensions in Millimeter (产品尺寸：mm）

| Part Number | A | B | C | D | E |
| --- | --- | --- | --- | --- | --- |
|  | Min | Max | Min | Max | Min | Max | Min | Max | Min | Max |
| SMD1206-110 | -- | 3.50 | -- | 1.85 | -- | 0.8 | 0.25 | -- | 0.10 | -- |
| SMD1206-125 | -- | 3.50 | -- | 1.85 | -- | 0.8 | 0.25 | -- | 0.10 | -- |
| SMD1206-150 | -- | 3.50 | -- | 1.85 | -- | 0.8 | 0.25 | -- | 0.10 | -- |
| SMD1206-175 | -- | 3.50 | -- | 1.85 | -- | 0.8 | 0.25 | -- | 0.10 | -- |
| SMD1206-200 | -- | 3.50 | -- | 1.85 | -- | 0.8 | 0.25 | -- | 0.10 | -- |
| SMD1206-230 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| SMD1206-260 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| SMD1206-300 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| SMD1206-350 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| SMD1206-380 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |

| SMD1206-400 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SMD1206-450 | -- | 3.50 | -- | 1.85 | -- | 1.0 | 0.25 | -- | 0.10 | -- |
| SMD1206-500 | -- | 3.50 | -- | 1.85 | -- | 1.2 | 0.25 | -- | 0.10 | -- |
| SMD1206-550 | -- | 3.50 | -- | 1.85 | -- | 1.3 | 0.25 | -- | 0.10 | -- |
| SMD1206-600 | -- | 3.50 | -- | 1.85 | -- | 1.3 | 0.25 | -- | 0.10 | -- |
| SMD1206-650 | -- | 3.50 | -- | 1.85 | -- | 1.3 | 0.25 | -- | 0.10 | -- |
| SMD1206-700 | -- | 3.50 | -- | 1.85 | -- | 1.4 | 0.25 | -- | 0.10 | -- |
| SMD1206-750 | -- | 3.50 | -- | 1.85 | -- | 1.4 | 0.25 | -- | 0.10 | -- |
| SMD1206-800 | -- | 3.50 | -- | 1.85 | -- | 1.4 | 0.25 | -- | 0.10 | -- |
| SMD1206-850 | -- | 3.50 | -- | 1.85 | -- | 1.4 | 0.25 | -- | 0.10 | -- |
| SMD1206-900 | -- | 3.50 | -- | 1.85 | -- | 1.5 | 0.25 | -- | 0.10 | -- |
| SMD1206-950 | -- | 3.50 | -- | 1.85 | -- | 1.5 | 0.25 | -- | 0.10 | -- |
| SMD1206-1000 | -- | 3.50 | -- | 1.85 | -- | 1.5 | 0.25 | -- | 0.10 | -- |

Electrical Characteristics（电气性能）

| Part Number | I(A) | Vmax | I max | Pdtyp | Ttrip | Rmin | R1max | R2max | R3max |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 25℃ | -- | -- | -- | 25℃ | 25℃ |
|  | Hold | Trip | (V) | (A) | (W) | Current(A) | Time(S) | (Ω) | (Ω) | (Ω) | (Ω) |
| SMD1206-110 | 1.10 | 2.2 | 6.0 | 50 | 1.2 | 8.0 | 0.5 | 0.008 | 0.055 | 0.060 | 0.065 |
| SMD1206-125 | 1.25 | 2.5 | 6.0 | 50 | 1.2 | 8.0 | 1.0 | 0.007 | 0.050 | 0.055 | 0.060 |
| SMD1206-150 | 1.50 | 3.0 | 6.0 | 50 | 1.2 | 8.0 | 5.0 | 0.006 | 0.045 | 0.050 | 0.055 |
| SMD1206-175 | 1.75 | 3.5 | 6.0 | 50 | 1.2 | 8.0 | 5.0 | 0.005 | 0.040 | 0.045 | 0.050 |
| SMD1206-200 | 2.00 | 4.0 | 6.0 | 50 | 1.2 | 8.0 | 5.0 | 0.004 | 0.035 | 0.040 | 0.045 |
| SMD1206-230 | 2.30 | 4.6 | 6.0 | 50 | 1.2 | 8.0 | 5.0 | 0.004 | 0.030 | 0.035 | 0.040 |
| SMD1206-260 | 2.60 | 5.2 | 6.0 | 50 | 1.2 | 12.0 | 5.0 | 0.003 | 0.025 | 0.030 | 0.035 |
| SMD1206-300 | 3.00 | 6.0 | 6.0 | 50 | 1.2 | 12.0 | 5.0 | 0.003 | 0.024 | 0.027 | 0.030 |
| SMD1206-350 | 3.50 | 7.0 | 6.0 | 50 | 1.2 | 12.0 | 5.0 | 0.002 | 0.018 | 0.021 | 0.025 |
| SMD1206-380 | 3.80 | 7.6 | 6.0 | 50 | 1.2 | 12.0 | 5.0 | 0.002 | 0.015 | 0.017 | 0.020 |
| SMD1206-400 | 4.00 | 8.0 | 6.0 | 50 | 1.5 | 16.0 | 5.0 | 0.001 | 0.011 | 0.015 | 0.018 |
| SMD1206-450 | 4.50 | 9.0 | 6.0 | 50 | 1.5 | 16.0 | 5.0 | 0.001 | 0.010 | 0.013 | 0.015 |
| SMD1206-500 | 5.00 | 10.0 | 6.0 | 50 | 1.5 | 16.0 | 5.0 | 0.001 | 0.009 | 0.011 | 0.012 |
| SMD1206-550 | 5.50 | 11.0 | 6.0 | 50 | 1.5 | 16.0 | 5.0 | 0.001 | 0.008 | 0.010 | 0.011 |
| SMD1206-600 | 6.00 | 12.0 | 6.0 | 50 | 1.5 | 20.0 | 5.0 | 0.0008 | 0.007 | 0.009 | 0.010 |
| SMD1206-650 | 6.50 | 13.0 | 6.0 | 50 | 1.5 | 20.0 | 5.0 | 0.0008 | 0.007 | 0.008 | 0.009 |
| SMD1206-700 | 7.00 | 14.0 | 6.0 | 50 | 1.6 | 20.0 | 5.0 | 0.0005 | 0.006 | 0.008 | 0.009 |
| SMD1206-750 | 7.50 | 15.0 | 6.0 | 50 | 1.6 | 20.0 | 5.0 | 0.0005 | 0.005 | 0.007 | 0.008 |
| SMD1206-800 | 8.00 | 16.0 | 6.0 | 50 | 1.6 | 20.0 | 5.0 | 0.0005 | 0.005 | 0.006 | 0.007 |
| SMD1206-850 | 8.50 | 17.0 | 6.0 | 50 | 1.6 | 20.0 | 5.0 | 0.0005 | 0.0045 | 0.006 | 0.007 |
| SMD1206-900 | 9.00 | 18.0 | 6.0 | 50 | 1.8 | 30.0 | 5.0 | 0.0004 | 0.004 | 0.005 | 0.006 |
| SMD1206-950 | 9.50 | 19.0 | 6.0 | 50 | 1.8 | 30.0 | 5.0 | 0.0003 | 0.0035 | 0.005 | 0.006 |
| SMD1206-1000 | 10.00 | 20.0 | 6.0 | 50 | 1.8 | 30.0 | 5.0 | 0.0002 | 0.003 | 0.004 | 0.005 |

IH=Hold current: maximum current at which the device will not trip at  25℃ still air.

保持电流=器件在25℃空气中不会关断的最大电流。

IT=Trip current: minimum current at which the device will always trip at  25℃  still air .

动作电流=器件在25℃空气中会关断的最小电流。

Vmax=Maximum continuous voltage device can withstand without damage at rated current

最大电压=器件在额定电流下可以承受的最高电压。

Imax=Maximum fault current device can withstand without damage at rated voltage.

最大电流=器件在额定电压下可以承受的最高电流。

Ttrip=Maximum time to trip(s) at assigned current.

动作时间：器件在指定电流下的关断时间。

Pdtyp=Typical power dissipation: typical amount of power dissipated by the device when in state air environment.

典型功耗：器件在空气环境下的典型功耗。

Rmin= Minimum resistance of device in initial (un-soldered) state.

最小阻值：器件在初始（未焊接）状态下的最小电阻。

R1max=Maximum resistance of device resistance range measured in the nontripped state 1 hour post reflow.

一次焊接的最大阻值:一次回流焊后未关断状态下测量的器件电阻范围的最大电阻。

R2max=Maximum resistance of device resistance range measured in the nontripped state 1 hour post twice reflow.

两次焊接的最大阻值:两次回流焊后未关断状态下测量的器件电阻范围的最大电阻

R3max=Maximum resistance of device resistancerange measured in the nontripped state 1 hour post twice reflow then curing 140℃/15min.

高温冲击的最大阻值：固化140℃15min,1小时后为关断状态下测量的器件最大电阻范围。

Caution: Operation beyond the specified rating may result in damage and possible arcing and flame.

警告：超过规定额定值的操作可能导致损坏，可能产生电弧和火焰。

Environmental Specifications （环境规范）

| Test | Test Conditions | Accept /Reject Criteria |
| --- | --- | --- |
| Recommended storage conditions 储存条件 | 40°C max, 70% R.H. max 最高温度40℃，最高湿度70% | No change 无变化 |
| Passive aging: 老化 | 85°C, 1000 hours 85℃，1000小时 | ≤ R3max ≤R3max |
| Moisture Resistance 高温高湿 | 85% RH,85℃,1000hrs 湿度85%，85℃ 1000小时 | ≤ R3max ≤ R3max |
| Gold and hot Shock 冷热冲击 | MIL-STD-202 Method 107G +85ºC /-40ºC 24 times 85℃/-40℃24次循环 | ≤ R3max ≤ R3max |
| Vibration 振动 | MIL-STD-883C, Method 2007.1, Condition A 标准：MIL-STD-883C 2007版 | No change 无变化 |
| Solvent Resistance 耐溶剂性 | MIL-STD-202, Method 215 标准：MIL-STD-202, 215 | No change 无变化 |
| Moisture Level Sensitivity 敏感湿度等级 | Level 2, J-STD-020C 等级2 | No change 无变化 |

Thermal Derating [ Hold Current (A) and Trip Current at Ambient Temperature (℃)（不同温度保持关断电流A）

| Part Number | Maximum Ambient Operating Temperature (℃) |
| --- | --- |
|  | -40 | -20 | 0 | 25 | 40 | 50 | 60 | 70 |
| SMD1206-110 | Ihold | 1.5 | 1.3 | 1.2 | 1.1 | 0.9 | 0.8 | 0.7 | 0.6 |
|  | Itrip | 3.0 | 2.6 | 2.4 | 2.2 | 1.8 | 1.6 | 1.4 | 1.2 |

| SMD1206-125 | Ihold | 1.7 | 1.5 | 1.4 | 1.25 | 1.1 | 1.0 | 0.9 | 0.7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Itrip | 3.4 | 3.0 | 2.8 | 2.5 | 2.2 | 2.0 | 1.8 | 1.4 |
| SMD1206-150 | Ihold | 2.0 | 1.8 | 1.6 | 1.5 | 1.2 | 1.1 | 1.0 | 0.9 |
|  | Itrip | 4.0 | 3.6 | 3.2 | 3.0 | 2.4 | 2.2 | 2.0 | 1.8 |
| SMD1206-175 | Ihold | 2.3 | 2.0 | 1.9 | 1.75 | 1.4 | 1.3 | 1.2 | 1.0 |
|  | Itrip | 4.6 | 4.0 | 3.8 | 3.5 | 2.8 | 2.6 | 2.4 | 2.0 |
| SMD1206-200 | Ihold | 2.7 | 2.3 | 2.2 | 2.0 | 1.6 | 1.5 | 1.4 | 1.1 |
|  | Itrip | 5.4 | 4.6 | 4.4 | 4.0 | 3.2 | 3.0 | 2.8 | 2.2 |
| SMD1206-230 | Ihold | 3.1 | 2.7 | 2.5 | 2.3 | 1.9 | 1.7 | 1.6 | 1.3 |
|  | Itrip | 6.2 | 5.4 | 5.0 | 4.6 | 3.8 | 3.4 | 3.2 | 2.6 |
| SMD1206-260 | Ihold | 3.5 | 3.0 | 2.8 | 2.6 | 2.1 | 1.9 | 1.8 | 1.5 |
|  | Itrip | 7.0 | 6.0 | 5.6 | 5.2 | 4.2 | 3.8 | 3.6 | 3.0 |
| SMD1206-300 | Ihold | 4.0 | 3.5 | 3.2 | 3.0 | 2.5 | 2.2 | 2.0 | 1.7 |
|  | Itrip | 8.0 | 7.0 | 6.4 | 6.0 | 5.0 | 4.4 | 4.0 | 3.4 |
| SMD1206-350 | Ihold | 4.7 | 4.1 | 3.8 | 3.5 | 2.9 | 2.6 | 2.4 | 2.0 |
|  | Itrip | 9.4 | 8.2 | 7.6 | 7.0 | 5.8 | 5.2 | 4.8 | 4.0 |
| SMD1206-380 | Ihold | 5.1 | 4.4 | 4.1 | 3.8 | 3.1 | 2.8 | 2.6 | 2.2 |
|  | Itrip | 10.2 | 8.8 | 8.2 | 7.6 | 6.2 | 5.6 | 5.2 | 4.4 |
| SMD1206-400 | Ihold | 5.4 | 4.7 | 4.3 | 4.0 | 3.3 | 3.0 | 2.7 | 2.3 |
|  | Itrip | 10.8 | 9.4 | 8.6 | 8.0 | 6.6 | 6.0 | 5.4 | 4.6 |
| SMD1206-450 | Ihold | 6.0 | 5.3 | 4.9 | 4.5 | 3.7 | 3.3 | 3.1 | 2.6 |
|  | Itrip | 12.0 | 10.6 | 9.8 | 9.0 | 7.4 | 6.6 | 6.2 | 5.2 |
| SMD1206-500 | Ihold | 7.5 | 6.5 | 5.5 | 5.0 | 4.5 | 3.5 | 3.3 | 3.0 |
|  | Itrip | 15.0 | 13.0 | 11.0 | 10.0 | 9.0 | 7.0 | 6.6 | 6.0 |
| SMD1206-550 | Ihold | 8.3 | 7.2 | 6.1 | 5.5 | 5.0 | 3.9 | 3.6 | 3.3 |
|  | Itrip | 16.6 | 14.4 | 12.2 | 11.0 | 10.0 | 7.8 | 7.2 | 6.6 |
| SMD1206-600 | Ihold | 9.0 | 7.8 | 6.6 | 6.0 | 5.4 | 4.2 | 3.9 | 3.6 |
|  | Itrip | 18.8 | 15.6 | 13.2 | 12.0 | 10.8 | 8.4 | 7.8 | 7.2 |
| SMD1206-650 | Ihold | 9.8 | 8.5 | 7.2 | 6.5 | 5.9 | 4.6 | 4.2 | 3.9 |
|  | Itrip | 19.6 | 17.0 | 14.4 | 13.0 | 11.8 | 9.2 | 8.4 | 7.8 |
| SMD1206-700 | Ihold | 10.5 | 9.1 | 7.7 | 7.0 | 6.3 | 4.9 | 4.6 | 4.2 |
|  | Itrip | 21.0 | 18.2 | 15.4 | 14.0 | 12.6 | 9.8 | 9.2 | 8.4 |
| SMD1206-750 | Ihold | 11.3 | 9.8 | 8.3 | 7.5 | 6.8 | 5.3 | 4.9 | 4.5 |
|  | Itrip | 22.6 | 19.6 | 16.6 | 15.0 | 13.6 | 10.6 | 9.8 | 9.0 |
| SMD1206-800 | Ihold | 12.0 | 10.4 | 8.8 | 8.0 | 7.2 | 5.6 | 5.2 | 4.8 |
|  | Itrip | 24.0 | 20.8 | 17.6 | 16.0 | 14.4 | 11.2 | 10.8 | 9.6 |
| SMD1206-850 | Ihold | 12.8 | 11.1 | 9.4 | 8.5 | 7.7 | 6.0 | 5.5 | 5.1 |
|  | Itrip | 25.6 | 22.2 | 18.8 | 17.0 | 15.4 | 12.0 | 11.0 | 10.2 |
| SMD1206-900 | Ihold | 13.5 | 11.7 | 9.9 | 9.0 | 8.1 | 6.3 | 5.9 | 5.4 |
|  | Itrip | 27.0 | 23.4 | 19.8 | 18.0 | 16.2 | 12.6 | 11.8 | 10.8 |
| SMD1206-950 | Ihold | 14.3 | 12.4 | 10.5 | 9.5 | 8.6 | 6.7 | 6.2 | 5.7 |
|  | Itrip | 28.6 | 24.8 | 21.0 | 19.0 | 17.2 | 13.4 | 12.4 | 11.4 |
| SMD1206-1000 | Ihold | 15.0 | 13.0 | 11.0 | 10.0 | 9.0 | 7.0 | 6.5 | 6.0 |
|  | Itrip | 30.0 | 26.0 | 22.0 | 20.0 | 18.0 | 14.0 | 13.0 | 12.0 |

Solder Reflow Recommendation  (推荐的回流焊曲线）

Recommended reflow methods:IR,hot air oven ,nitrogen oven

推荐回流焊方式：红外线、热风烘箱、氮气烘箱。

Devices can be cleaned using standard industry methods and solvents.

设备可以使用标准的工业方法和溶剂进行清洗。

NOTE:

注意：

If reflow temperatures exceed the recommended profile,devices may not meet the performance requirements.

如果回流焊温度超过推荐的温度，期间可能无法满足性能要求。

Caution: Operation beyond the rated voltage or current may result in rupture electrical arcing or flame

警告：超过额定电压或电流的操作可能导致器件破裂、电弧或燃烧。

Packaging Quantity and Marking （包装数量及标识）

| Device 器件 | Marking 标识 | Standard Quantity (pcs) 包装数量 |
| --- | --- | --- |
| SMD1206-110 | B 110 | 4000 |
| SMD1206-125 | B 125 | 4000 |
| SMD1206-150 | B 150 | 4000 |
| SMD1206-175 | B 175 | 4000 |
| SMD1206-200 | B 200 | 4000 |
| SMD1206-230 | B 230 | 4000 |
| SMD1206-260 | B 260 | 4000 |
| SMD1206-300 | B 300 | 4000 |
| SMD1206-350 | B 350 | 4000 |
| SMD1206-380 | B 380 | 4000 |
| SMD1206-400 | B 400 | 4000 |
| SMD1206-450 | B 450 | 4000 |
| SMD1206-500 | B 500 | 3000 |
| SMD1206-550 | B 550 | 3000 |
| SMD1206-600 | B 600 | 3000 |
| SMD1206-650 | B 650 | 3000 |
| SMD1206-700 | B 700 | 3000 |
| SMD1206-750 | B 750 | 3000 |
| SMD1206-800 | B 800 | 3000 |
| SMD1206-850 | B 850 | 3000 |
| SMD1206-900 | B 900 | 3000 |
| SMD1206-950 | B 950 | 3000 |
| SMD1206-1000 | B 1000 | 3000 |

Tape Specifications:EIA-481-1(mm) （编带标准：EIA481-1 mm）

| Governing Specifications | SMD1206-110~ SMD1206-450 | SMD1206-500~ SMD1206-1000 |
| --- | --- | --- |
| W | 8.0±0.3 | 8.0±0.3 |
| F | 3.5±0.05 | 3.5±0.05 |
| E1 | 1.75±0.1 | 1.75±0.1 |
| D0 | 1.55±0.05 | 1.55±0.05 |
| D1 | 1.0±0.1 | 1.0±0.1 |
| P0 | 4.0±0.1 | 4.0±0.1 |
| P1 | 4.0±0.1 | 4.0±0.1 |
| P2 | 2.0±0.05 | 2.0±0.05 |
| A0 | 1.95±0.1 | 1.95±0.1 |
| B0 | 3.65±0.1 | 3.65±0.1 |
| T | 0.2±0.1 | 0.2±0.1 |
| K0 | 0.87±0.1 | 1.3±0.1 |
| Leader min | 390 | 390 |
| Trailer min | 160 | 160 |

Reel Dimensions:EIA-481-1(mm) 卷盘尺寸：EIA-481-1标准

| Governing Specifications | EIA481-1 |
| --- | --- |
| C | Φ178±1.0 |
| D | Φ60.2±0.5 |
| H | 11.0±0.5 |
| W | 9.0±1.5 |

NOTE:

BNstar Co.,Ltd. makes no representations or warranties with respect to the accuracy or completeness of the contents of

this publication and reserves the right to make changes to specifications and product descriptions at any time without

notice. The products described in this document are not designed, intended, authorized or warranted for use as components in systems intended for surgical implant into the body, or in other applications intended to support or sustain life, or where malfunction of BNstar’s product may result in direct physical harm, injury, or death to a person or severe property or environmental damage. BNstar Co.,Ltd., reserves the right to discontinue or make changes to its products at any time without notice.

比诺星新材料有限公司对此规格书内容的准确性或完整性不作任何保证，并保留在不另行通知的情况下随时更改规格和产

品描述的权利。本规格书描述的产品不涉及、授权或保证用于人体外科设备植入中，或用于支持和维持生命的其他应用。比诺星产品的故障可能导致直接的物理伤害或造成人员死亡或严重的财产损失或环境破坏。比诺星公司有权随时停止或更改其产品而不另行通知。

Website: http://www.bnstar.net

网站： http://www.bnstar.net

For additional information, please contact your local Sales Representative.

如需更多信息，请与您当地的销售代表联系。

©Copyright 2006, BNstar Co.,Ltd.

上海比诺星新材料科技有限公司版权所有

| Rev. letter |  | Date |  |
| --- | --- | --- | --- |
| Design | Check | Audit | Approve |

Contact information（联系我们）

BNSTAR NEW MATERIALS CO., LTD.

上海比诺星新材料科技有限公司

130Meilong  Road Shanghai, P.R.China

中国，上海梅陇路130号

Tel:86-021-64251576    Fax: 86-021-64250020

EMAIL：info@bnstar.net

SMD PTC使用注意事项

Cautions for SMD ptc Use

- 请在规格书规定的最大电压和最大电流下使用，超出PTC最大电压或最大电流规格值的操作，可能会导致PTC出现电弧，阻值升高，甚至烧片。

Operation beyond the maximum voltage or current may result in device damage and possible electrical arcing or flame.

- 规格书所规定的各温度下的维持电流均是PTC经过一次回流焊接得出的常规性能,PTC能够在不同温度对应的电流条件下保持1小时。该电流并不是该型号PTC能够适用的长期充电或放电电流的条件。

Hold current at all temperatures specified in the SPEC is the conventional performance of PTC obtained by one time reflow welding.PTC can hold 1hour under current conditions at a given temperature .This current is not the condition of long-term charging or discharging current for this type of PTC.

- 规格书所规定的电阻以及电气特性，均是基于在比诺星指定测试板经过一次回流焊之后的测试。如果客户有二次回流焊或者注塑点胶等其他热工序，会对上述参数有一定程度的衰减，所以需要验证其适用性。

The above parameters are concluded from one time of reflows soledring processing the PTC.If there is any further heat generated process like injection or dispensing at the customer’s premise ,the aforementioned parameters will decrease at certain degree.Therefore the verification test to be conducted is necessary.

- PTC为热敏元件，对环境温度比较敏感，建议在PTC周围不要设计热源元件，尽量减少外部热源的影响。

The PTC is thermal sensitive device.It is recommended not to design any heat source devices around it to reduce the outside heat source impact.

- PTC贴片产品是为SMT工艺设计的封装形式，焊接工艺为回流焊。焊接工艺可参考比诺星推荐的回流焊曲线。如果回流焊温度超过推荐的值，PTC将有可能受到损伤。禁止使用手工焊接PTC，禁止对线路板其他元件或端子返工时使用热风枪。

SMD PTC is designed for SMT processing which applies reflow soldering.Please refer to the Bnstar recommended curve for reference.If the reflow soldering temperature exceeds the recommended value,the PTC might be damaged.Hand welding PTC is prohibited.Heat gun is not allowed to use during the circuit board componenrs or terminals rework.

- PTC贴装或应用过程中，所使用到的各类注塑料、单组份、双组份固化剂、硅胶，需要对注塑料等材料牌号以及应用参数(如温度、时间等）进行验证，以确保产品及工艺的匹配性，确认不会影响PTC性能之后方可使用。

When mounting or using PTC,all injection molding materals,curing adhesives,UV glue,silica gel and cleaning agents or solvents must be tested in terms of application parameters e.g.temperature,time,and etc to ensure the consistency between the product and the processing before use.

7、PTC贴装或使用过程中，不建议使用洗板水或其他清洗剂进行清洗。如必须使用，需要验证各类清洗剂、洗板水以及溶剂的适用性，确定不会影响PTC性能之后方可使用。已知对PTC有影响的化学药品包含但不仅限于醚类、苯类、酮类以及脂类等较强溶解性、破坏性的有机化合物。清洗后将产品放置于敞开的环境中至少24小时，将残留的溶剂进行充分的挥发。

When mounting or using PTC,it is not recommended to use circuit board washer water or other cleaning agent. If cleaning is required ,iit is necessary to verify the applicability of various cleaning agents,washboard water and solvents,and confirm that they will not affect the PTC performance.The known chemicals that impacts PTC include but not limited to ethers,benzene homolog,ketones,lipids and derivates that is of strong solubleness and ruinous.please place the product in open envieonment for at lesst 24 hours to volatilize solvents residuals.

8、装配过程中，避免用暴力砸、挤、压、拉、扭、刺等方式作用PTC本体，以免引起PTC性能衰减。

Please do not smash,clamp,pull,dent or twist by tool during assembling process otherwise it mighet it might be a cause of the performmance degradation.

- 在产品应用中，PTC焊接至保护板后，如需注塑或打胶，须在尽量短的时间内完成，如贴装与注塑打胶时间间隔超过一个月，则需密封保存，可避免PTC长时间暴露于空气环境中。

When PTC is welded to the PCM in product application,if injection or gluing is needed,it should be completed in as short a time as possible.If the time slot between mounting and injection or gluing surpasses 1 month,please keep in airtight environment to avoid long air exposure.

- PTC为自恢复保护元件，但并不能当作开关使用，重复多次的保护会降低PTC的维持电流。

PTC is resettable protection device which shall not be taken for use as switch.Multiple times tripping shall lower the PTC hold current.

- PTC在充电线端应用中，建议使用PP类材料做内膜，禁止使用TPE类与PVC类等材料做内膜。

In charging terminal application,PP type material is recommended to use as inner membrane and TPE and PVC type material is inhibited.

- PTC在加工工程中，如有洛铁焊接工艺，建议焊接位置距离PTC1.5mm以上，焊接工具温度低于350℃，焊接头与焊点的接触时间不超过3秒。

In the process of PTC processing,if there is soldering iron welding process,it is suggested that the welding position should be more than 1.5mm away from PTC,the welding tool temperature should be lower than 350℃，and the contact time between soldring iron and solder joint should not exceed 3 sec.

- 比诺星低阻SMD PTC敏感湿度等级为2级，为密封包装。客户如在库存中发现有包装破损的，立即将产品隔离处理，使用时如有余料，需要恢复之前包装状态做密封保存。

Bnstar low resisitance SMD PTC humidity sensitivity grade2,for sealed packaging.If customers find damaged packing in stock,they should isolate the product immediately,if there is surplus material,they need to restore the packaging status,and do sealed storage.